## Slide 1: A compensation technique for accurate acceleration measurements using a UAV-deployable and retrievable sensor package
Methodology
Experimentation
Results and Discussion
Future work
Joud Satme; Department of Mechanical Engineering Corinne Smith; Department of Mechanical Engineering Austin R.J. Downey; Department of Mechanical, Civil and Environmental Engineering Jason D. Bakos; Department of Computer Science and Engineering Nikolaos Vitzilaios; Department of Mechanical Engineering Dimitris Rizos; Department of Civil and Environmental Engineering

## Slide 2
Methodology
Experimentation
Results and Discussion
Outline
Methodology:
  Sensor package breakdown
    Features
    Hardware
    Algorithm
  Deployment and retrieval
  Transfer function-based filter
    Approach and assumptions
    Model training
Experimentation:
  Bench-top testing (Training)
  Structure testing (Validation)
Results and Discussion:
  Experimental outcomes
  Findings and limitations
Future work:
  Sensor improvement
  Edge implementation
2
Future work

## Slide 3
Methodology
Experimentation
Results and Discussion
Introduction
Importance of structural health monitoring.
Current systems in use and their features.
Problem statement:
  Long-term data collection.
  Rapid large-scale deployment.
  Transmissibility losses.
Proposed approach:
  Stand-alone sensor package.
  UAV-delivery system.
  Transfer function-based compensation method.
3
Future work

## Slide 4
Methodology
Experimentation
Results and Discussion
Sensor package breakdown
Features:
  UAV deployable sensor package designed with high mobility in mind.
  Power and memory storage subsystems in anticipation of long-term deployment.
  Wireless subsystem for data transmission and IO commands.
  Docking subsystem utilizing electropermanent magnets.
  Frame of the package designed with minimizing transmissibility losses in mind.
  Maximum sampling rate 28 kS/s.
4
Future work

## Slide 5
Methodology
Experimentation
Results and Discussion
5
Sensor package breakdown
Hardware:
  Processor: ARM Cortex-M7 on Teensy 4.0 microcontroller.
  SCA3300-d01 MEMS accelerometer.
  EPM V3R5C electropermanent magnet.
  Nonvolatile memory (SD card) for long-term storage.
  Lithium polymer battery, voltage regulation and monitoring.
  NRF24L01 Nordic Semiconductor wireless transceiver.
Future work

## Slide 6
Methodology
Experimentation
Results and Discussion
Sensor package breakdown
Developed on Arduino IDE and deployed on an ARM Cortex-M7 processor.
Algorithm:
  Initialize the magnet signaling start of deployment.
  Acceleration data is periodically collected.
  Data collected in a buffer to enable high sampling rates.
  74,000 timed samples are collected then transferred onto the memory.
  Code initiates standby mode which turns modules off to conserve power.
  Microcontroller and wireless module remain on for communication.
User interface:
  A connection is achieved over 2.4 GHz ShockBurst protocol.
  User can monitor operating conditions of the sensor package.
  Retrieve stored data.
  Issue commands to electropermanent magnet for retrieval.
6
Future work

## Slide 7
Methodology
Experimentation
Results and Discussion
7
Deployment and retrieval
Package is mounted onboard UAV.
Contact is established with test structure.
Electropermanent magnet on sensor package initiates.
UAV electropermanent magnet disengages.
Sensor package periodically collects data.
UAV approaches structure and establishes contact with package.
Electropermanent magnets toggle.
UAV retrieves sensor package.
Future work

## Slide 8
Methodology
Experimentation
Results and Discussion
Transfer function-based filter
Approach and assumptions:
  Input-output relationship is acquired using frequency sweep excitation (Chirp).
  A model of the physical sensor package () is created.
  Assumptions made about the plant :
    Linearity
    Causality
    Minimal-phase system
  is inversed creating the filter .
  Using , the influence of the plant is attenuated.
  True acceleration obtained given only the output of .
8
Future work

## Slide 9
Methodology
Experimentation
Results and Discussion
Transfer function-based filter
Model Training:
  Using a chirp function:
    frequency sweep function
  Excitation using electromagnetic shaker
9
Future work

## Slide 10
Methodology
Experimentation
Results and Discussion
  Bench-top testing (Training)
  Experimental parameters:
    Bandwidth of interest: 0.1-20.9 Hz
    Excitation source: Electromagnetic shaker
    Reference accelerometer: Piezoelectric model 393B04
    Sensor package hard-wired trigger.
    Sampling rate: 1600 S/s
10
Future work

## Slide 11
Methodology
Experimentation
Results and Discussion
  Bench-top testing (Training)
  Experimental procedure:
    Synthesized Chirp voltage signal is fed into the shaker for excitation.
    Reference accelerometer and sensor package are synchronized
    Through this experiment an input-output relationship is established.
11
Future work

## Slide 12
Methodology
Experimentation
Results and Discussion
12
zz
Future work
  Bench-top testing (Training)
  Model training:
    Multiple data sets are used in modeling.
    Input: Reference accelerometer
    Output: Sensor package
    Transfer function model is constructed.
    Transfer function is then inversed creating the filter.
  Inverse plant transfer function:

## Slide 13
Methodology
Experimentation
Results and Discussion
  Structure test (Validation)
  Experimental parameters:
    Steel test structure is constructed.
    Data acquisition system:
      Analog output generate excitation signal.
      Digital trigger to synchronize sensor package and reference accelerometer.
      Data logging of reference acceleration.
    Signal-to-noise ration was used to measure performance.
13
Future work

## Slide 14
Methodology
Experimentation
Results and Discussion
  Structure test (Validation)
  Experimental procedure:
    The sensor package is mounted onto test structure along with a reference accelerometer.
    The electromagnetic shaker is secured on top as the source of excitation.
    The package and reference accelerometers are triggered.
    Chirp signal is then used to excite the structure.
    Sensor package data is examined with and without filtering to gauge performance.
14
Future work

## Slide 15
Methodology
Experimentation
Results and Discussion
Experimental outcomes
Structure test (Validation):
  Filtered signal traces the reference with high correlation.
  Frequency domain indicates enhancement in the range of 6-20 Hz.
  Error percentage is considered negligible between 6-14 Hz (<0.4%).
  Signal-to-noise ratio pre and post filtering is shown.
15
Future work

## Slide 16
Methodology
Experimentation
Results and Discussion
Structure test (Validation)
Findings and limitations:
  Diminishing returns of the filter can be observed in the range below 5 Hz.
  Analog-to-digital converter (ADC) lack adequate resolution to detect the low-energy signal found in lower frequencies.
16
Future work

## Slide 17
Methodology
Experimentation
Results and Discussion
Future work
Future work
  Sensor improvement
    Improve resolution of analog to digital converter onboard the sensor package.
    Investigate sensor network deployment.
  Edge implementation
    Discretize transfer-function filter.
    Investigate the feasibility of microcontroller implementation.
On-edge
17

## Slide 18
Thank you
Questions?
Author Information
Name: Joud Satme
Email: Jsatme@email.sc.edu

## Slide 19
References:
[1] Pakzad, S. N., Fenves, G. L., Kim, S., and Culler, D. E., “Design and implementation of scalable wireless
sensor network for structural monitoring,” Journal of Infrastructure Systems 14, 89–101 (mar 2008).
[2] Sabato, A., Niezrecki, C., and Fortino, G., “Wireless mems-based accelerometer sensor boards for structural
vibration monitoring: A review,” IEEE Sensors Journal 17(2), 226–235 (2017).
[3] Carroll, S., Satme, J., Alkharusi, S., Vitzilaios, N., Downey, A., and Rizos, D., “Drone-based vibration
monitoring and assessment of structures,” Applied Sciences 11(18) (2021).
[4] Takeuchi, K., Masuda, A., Akahori, S., Higashi, Y., and Miura, N., “A close inspection and vibration sensing
aerial robot for steel structures with an EPM-based landing device,” in [Nondestructive Characterization
and Monitoring of Advanced Materials, Aerospace, and Civil Infrastructure 2017], Wu, H. F., Gyekenyesi,
A. L., Shull, P. J., and Yu, T.-Y., eds., 10169, 666 – 677, International Society for Optics and Photonics,
SPIE (2017).
[5] Chen, B. and Liu, W., “Mobile agent computing paradigm for building a flexible structural health monitoring
sensor network,” Computer-Aided Civil and Infrastructure Engineering 25, 504–516 (aug 2010).
[6] Badri, A. E., Sinha, J. K., and Albarbar, A., “A typical filter design to improve the measured signals from
mems accelerometer,” Measurement 43(10), 1425–1430 (2010).
[7] Karpel, M. and Ricci, S., “Experimental modal analysis of large structures by substructuring,” Mechanical
Systems and Signal Processing 11(2), 245–256 (1997).
[8] Sim, S.-H., Li, J., Jo, H., Park, J.-W., Cho, S., Jr, B. F. S., and Jung, H.-J., “A wireless smart sensor
network for automated monitoring of cable tension,” Smart Materials and Structures 23, 025006 (dec 2013).
[9] Ubertini, F., Comanducci, G., and Cavalagli, N., “Vibration-based structural health monitoring of a historic bell-tower using output-only measurements and multivariate statistical analysis,” Structural Health
Monitoring 15(4), 438–457 (2016).
[10] Johnson, D. H., “Signal-to-noise ratio,” Scholarpedia 1(12), 2088 (2006). revision #126771.
[11] Ljung, L., System Identification Toolbox (2014)